Raspberry Pi Workshop

NOV 2014

(C) Peter Rogers
Creative Commons License
Attribution-Non commercial

About this workshop
-Summary
-This workshop will introduce you to the Raspberry Pi, an inexpensive single-board computer designed for educational and hobbyist use.
-The workshop is aimed at hobbyists, artists and makers who wish to incorporate the Pi into their projects.

What comes in the kit
-Raspberry Pi Model B+
-Micro USB cable
-Micro SD card preloaded with Linux
-Resistors
-Servo
-Ultra-sonic range finder
-Pi breakout / protection board
-Hall-effect transistor
-MOSFETs
-LEDs
-Thermistor
-Photoresistor

Overview of the Raspberry Pi

- Created by the Raspberry PI foundation, a registered charity in the UK.
- Designed as an educational tool for students, hackers, makers
- Similar to the Arduino in some respects, also much more capable (and lacking in other respects)
- Four versions to date (A, A+, B, B+) - all very similar

Hardware breakdown:

- 512 MB RAM
- Broadcom system on a chip
- ARM based processor (most desktops are Intel based)
- Broadcom system on a chip (SoC)
- Boots OS from SD card (hard drive)
- 4x USB ports
- On-board Ethernet
- On-board audio jack (or audio is delivered via HDMI cable)
- USB connector for power (not data)
- Power light shows when power is connected (though the Pi may not necessarily be running)
- Hard disk activity light
- General Purpose IO header (digital input+output pins, much like Arduino) – 40 pins
- No analog input pins, only digital
- Linux installation – Debian (distribution) Wheezy (version)

Warnings – Care and Feeding

- The Pi can supply two voltages – 3.3v and 5v
- Don't feed 5v into the board, or bad things will happen
- Be careful of stray wires (disconnect from the PI first, then from your breadboard)
- Power down your PI properly before disconnecting the supply
- Be careful not to eject the SD when handling your Pi
- Avoid touching the Pi while it is powered
- Be careful plugging / unplugging USB devices when powered up. It's physically awkward when plugging them in. (lots of friction and slipping)

Installation

- Your kit comes with Linux pre-installed, updated and useful packages installed. (batteries mostly included)
- Install images are available online, and they must be copied onto an SD card using a separate computer
- Installation is not covered here
- See http://www.raspberrypi.org/downloads/ for disk images and instructions

A brief tour of the Pi

-Booting
-Setup instructions (config utility)
-Starting X
-Some useful built-in features
-Playing video, music, web browser
-Intro to the command-line
-Running programs as root
-Brief mention of python
-Emphasis: the raspberry pi is a full computer, just smaller
-Connect to monitor / TV with HDMI
-Using an adapter connect with VGA or DVI (most computer displays)
-What if you don't have a spare monitor? Or a display with HDMI?

Config utility

-raspi-config (starts after a fresh install, or run from command-line)
-Allows you to change some basic options
-Change the host name
-Enable/disable onboard peripherals
-Change audio output (through HDMI or the jack)

Connecting to the Pi remotely

Advantages
- You don't need a spare monitor
- Very portable – can develop on the go with a Pi + laptop
- Run the Pi off your laptop supply, no need for extra power
- Connect to Pi wirelessly (useful if the Pi is buried in your project)
- Run GUI applications remotely using X

Disadvantages
-No fancy graphics

-Connect via ssh or putty

Shutting down the Pi remotely
- Run the command: sudo shutdown -h now
- The command sudo runs as root (super-user)
- Shutdown is the utility for shutting down or rebooting, '-h' requests that the machine halts, and the time is 'now'

Finding your Pi on the network

-Run a discovery protocol on your PI (uses mDNS protocol)
-Linux: avahi-browse –all
-Windows: Install Bonjour
-MacOS: ?? (http://hints.macworld.com/article.php?story=20051026183044858)

Introduction to GPIO and Python
-Blinking LED example
-Wiring to breadboard
-Resistor and LED in series
-Protection board
-Python code to drive led
-Blink faster, slower, change duty cycle

Breadboards
-Fast prototyping (wire without soldering)
-Columns are common, top and bottom rows are common
-Jumper wire makes wiring test circuits very easy

PI safety shield
-Protected IO pins prevent you feeding in too much voltage (somewhat)
-Also prevents you from drawing too much current from pins
-Current limiting resistor prevents too much current draw
-Zener diode (backwards) clamps input voltage to 3.3V

LED example
-Connect LED to PI output pin
-Be careful to pick the right resistor, or you will draw too much current and blow the LED / blow the PI
-RGB LED example

Hall-effect transistor
-Switches in the presence of a magnetic field
-Useful for creating a switch that doesn't need physical contact
-Very close proximity sensor

Range-finder example
-Power with 5v (be careful!), returns a 5v signal
-Ultra-sonic sensor
-Send a pulse, time how long it takes to come back
-Estimate distance based on the speed of sound
-Not very accurate, has problems with some materials not reflecting sound (multiple reflections?)

Servo example
-PWM signal determines angle of rotation
-Motor has feedback so it “knows” where it is in the rotation
-Use servos to create robots, interactive pieces with moving parts

MOSFET example
-Driving an LED, multiple LEDs
-You need to be very careful when handling MOSFETs, they are very sensitive to ESD (electro-static discharge)
-Mishandling them can damange or destroy them very quickly
-We use a zener diode to protect them from accidental ESD (same component on the protection board)

Using the onboard ATTINY for extra functionality
-Analog to digital converter

Photo resistor example
-Measure light levels
-Drive LED based on light levels

Thermistor
-Resistor that changes resistance based on temperature (similar to a photo resistor)